## Slide 1: Atmospheric Sciences 370 Observing Systems Winter 2024
Observations are the foundation of synoptic meteorology

## Slide 2: Observation Terminology
Direct versus Indirect observations
  Direct: measurement at the location of the instrument
  Indirect: remotely sensed using radiation measurements
Direct: surface weather station, radiosonde
Indirect: satellite sensing of cloud-top temperatures.

## Slide 3: Observation Terminology
Active versus passive remote sensing
  Active: The instrument emits radiation, which interacts with target, and returns. Analyzes return
  Passive: analyzes incoming natural radiation
Radar is active
Infrared satellite imagery is passive.

## Slide 4: ASOS: Automated Surface Observing System Backbone Surface Observing System in the U.S.

## Slide 5: ASOS
Located at primary and secondary airports
Supported by the FAA and NWS
High-quality instrumentation that is well maintained and calibrated.
Reported in METAR format

## Slide 7
Hydrothermograph

## Slide 8
Precipitation Gauges
Many are shielded

## Slide 9: Some Even with Double Shields
Shields reduce wind and turbulent eddies around gauges which can lessen catch efficiency. The largest effect of wind is on snow.

## Slide 10: Catch Efficiency: Better for Shielded Gauges

## Slide 11
Laser Weather
Identifier
No human intervention!
Rain versus snow, etc.

## Slide 12
Acoustic Anemometer

## Slide 13
Anemometer
Wind Vane
Mechanical wind instruments no longer used in ASOS!
Suffered from icing.
Did not measure low speeds well.

## Slide 14
Laser Ceilometer
The ceiling is the height of the lowest cloud layer
Very important for aviation.

## Slide 15
Can Provide Vertical Profiles of Clouds and Smoke

## Slide 16
UW Ceilometer

## Slide 17: Can Sense Wildfire Smoke

## Slide 18
ASOS Pressure Sensor

## Slide 19: ASOS Pressure Sensors
Gold Standard
Three sensors, requires agreement of at least two.
Accuracy: +-.02 inches of mercury ( .67 hPa)
Resolution: .003 inches, .1 hPa

## Slide 20
The ASOS Freezing Rain Sensor
Uses an ultrasonically vibrating probe to detect the presence of icing conditions. The vibrating frequency of the probe decreases with the accumulation of ice.

## Slide 21
Lightning Sensor
Visibility Sensor

## Slide 22: Observing Heights (ASOS and Most Official Obs)
Temperature and dew point (2-m)
Wind speed and direction (10-m)

## Slide 23
Full ASOS system in Arizona

## Slide 24: METAR Format
ASOS data (and airport observations worldwide) are transmitted in METAR format.
Name came from the French words, MÉTéorologique ("Weather") Aviation Régulière ("Routine").
Example: KSEA 042353Z 11008KT 10SM FEW050 SCT070 OVC090 09/03 A2879 RMK AO2 SLP756 60001 T00940033 10117 20083 58013

## Slide 25: Many Other Surface Networks
Bureau of Land Management
RAWS
Agrimet
PAWS
Department of Ecology
Puget Sound Clean Air
BC Hydro
BC Olympics
Weather Underground
Many more!

## Slide 26
Oklahoma Mesonet

## Slide 27: New York Mesonet

## Slide 28
Networks of Networks
MesoWest: Collects about 100 networks over the western third of U.S.
MADIS: NOAA national collection of mesonets

## Slide 30: One of the best viewers of many networks: NOAA Weather/Hazards
https://www.wrh.noaa.gov/map/?obs=true&wfo=sew

## Slide 31: Consider
In 1980, there were approximately 1000 real-time surface observations in the U.S., mainly at airports
Today, with so many networks, there are several hundred thousand.

## Slide 32: Global Surface Observation Coverage

## Slide 33: Global Coverage: Many More Northern Hem.

## Slide 34: Marine Weather and Surface Ocean Reports

## Slide 35
Ocean and Lake
Weather Buoys
Anchored

## Slide 36: Drifting Buoys: Move Around!
Wind
Pressure

## Slide 37
Coastal Marine (CMAN) Reports from the Coast Guard

## Slide 38
Northwest Buoy and CMAN Locations

## Slide 41
Ship Reports: Marine VOS Program
Volunteers Observers--generally 6-hourly reports
Highly variable quality and frequency

## Slide 43: Satellite Microwave Scatterometers: Microwaves scattering off surface waves give surface wind and direction

## Slide 44
QuickScat Satellite
Bounces microwaves off the ocean surface
Capillary waves dependent on wind speed and direction

## Slide 45
Satellite
Microwave
Scatterometer
Winds

## Slide 47: Satellite scatterometers

## Slide 48: Upper Air Data

## Slide 49
Radiosondes
First launched in 1929

## Slide 50: Radiosondes
Provides temperature, humidity (relative humidity, pressure, and wind speed/direction)
Generally launched twice a day (00 and 12 UTC).

## Slide 51: Radiosondes
A typical NWS radiosonde sounding ascent can last 2-3 hours
In that time, the radiosonde can ascend to an altitude exceeding 35 km (about 115,000 feet) and drift more than 300 km (about 180 miles) from the release point.
Typical pressure at balloon burst about 5 hPa (1/200th of surface pressure).

## Slide 52: Generally launched twice a day at 00 and 12 UTC
About 1000 locations around the world

## Slide 53: There are websites that track them..

## Slide 54
Radar Wind Profiler and RASS (Radio Acoustic Sounding System)
Can provide temperature and wind with height
Can also provide information on precipitation/clouds

## Slide 58
ACARS: Aircraft Observations
Often on wide-body aircraft
Aircraft Communications Addressing and Reporting System

## Slide 59: Available at cruise altitude and ascent/descent.

## Slide 62: Also data from AIRDAT/Panasonic: Commuter and Short Haul Aircraft

## Slide 63: Weather Satellites Now Provide Roughly 99% of the Weather Data Going into Weather Prediction

## Slide 64: Satellite Data
Geostationary and Polar Orbiting Satellites

## Slide 65
GOES

## Slide 66: Geostationary Image

## Slide 67
Geostationary satellite see the whole hemisphere

## Slide 68
Putting them together, one can monitor the entire planet

## Slide 69
NOAA Polar
Orbiter Weather
Satellite
Polar Orbiter: Lower/higher resolution/more sensors

## Slide 70
Polar Orbiters Provide a High-Resolution View
A polar
low

## Slide 71: Weather Satellites Provide MUCH More Than Just Imagery

## Slide 72
Cloud and
Water Vapor
Track Winds
Based on Geostationary Weather Satellites

## Slide 74: Atmospheric Moisture Vectors from Satellites

## Slide 75
GOES sounder unit: observes atmosphere/earth’s emissions in several wavelengths

## Slide 76
Views the Earth
at many wavelengths,
each mainly sensing temperature at a specific layer

## Slide 77
Satellite Temperature and Humidity Soundings

## Slide 78: High-Resolution Infrared Radiation Sounder

## Slide 79: Microwave Sounders

## Slide 80: GPS Soundings
A constellation of GPS satellites orbit the earth.
A collection of special satellites can receive the GPS signal
By measuring the delay in time as the GPS signal is bent by the earth’s atmosphere, one can determine atmospheric density variations in the vertical that can be used to create temperature and humidity soundings.

## Slide 83
During the early 90s, the NWS installed a network of powerful Doppler Weather
radars, a.k.a.
NEXRAD
WSR88D
Weather Radar

## Slide 84: NWS Radar Sites

## Slide 85: Weather Radar
Reflectivity (precipitation intensity)
Doppler Velocities (radial velocities)
Polarimetric Information (precipitation type and other information?
Much more later in class

## Slide 86
Camano
Island
Weather
Radar

## Slide 87: Crowdsourcing of Weather Data
Securing weather data from devices intended for other purposes.
Example: pressure data from smartphones
Example: smartphone reported weather conditons

## Slide 88: Smartphone Pressures

## Slide 89: Weather Data from the Purple Air Air Quality Network

## Slide 90: mping: NWS effort of crowdsource weather observations

## Slide 91: A Synoptic Meteorologist Needs to Know The Accuracy of Various Observational Assets

## Slide 92: Typical Observation Errors at the Surface (Important when doing analyses!)
Sea Level Pressure
  Low-elevation land stations +-.5 mb
  Ships +- 1-5 mb
Temperature: +-1C
Wind Speed: +-2-5 knots, very light winds often a problem—especially for classical anomemeters.
Relative Humidity: +-10%

## Slide 93: Typical Radiosonde Errors
Geopotential heights:
  700 mb (hPa): 5-10 m
  500 mb 10-15 m
  300 mb 15-20 m
  100 mb 20-30 m
Temperature: +-0.5C
Wind speed: +-5%,+-10 degrees

## Slide 94: Some Terminology Often Used
Synoptic scale
Mesoscale
Microscale

## Slide 95: Synoptic Scale (1000 km and more)

## Slide 96: Mesoscale (10-1000 km)

## Slide 97: Microscale (smaller than 10 km)

## Slide 98: The END