## Slide 1: Weather Radar 101 Autumn 2024

## Slide 2: Weather Radar 101
Weather radars determine where precipitation is falling
Can also tell the intensity of the precipitation
Doppler radars can also determine the speed/velocity of precipitation toward or away from the radar.
Radars can track storms, fronts, and other major features
An essential tool for the National Weather Service and other meteorologists.

## Slide 3: Weather Radar Can Enhance Your Life If You Know How to Interpret it (You will!)

## Slide 4: What is Radar?
RAdio Detection And Ranging
Weather radars emit pulses of electromagnetic radiation in the microwave part of the electromagnetic spectrum
Radar wave pulses hit and are reflected/scattered back from targets (often precipitation)

## Slide 5: What is Radar?
RAdio Detection And Ranging
The time it takes to return tells the distance
The amount of return tells us about precipitation intensity and type

## Slide 6: Radar waves move at the speed of light (186,000 miles per second in a vacuum). Thus, the time from emission to return tells how far the object is away.

## Slide 7: The amount of radar signal returned tells one about the nature of the object: type and intensity of precipitation
Amount scattered back ~ D6 where D is the diameter of the target
Big objects (e.g., large rain drops associated with heavy rain)---big radar return
Small objects (small droplets)—lesser return
More objects—more return

## Slide 8: Thus, heavy rain with lots of big droplets give a big radar return!

## Slide 9: Reflectivity
A fancy name for the amount of radar signal that is returned by an object: reflectivity (Z) is given in units of dbZ
db or decibels-unit of power on a logarithmic scale
Precipitation intensity is proportional to Z (or dbZ)

## Slide 10: Reading a Radar Image
Intensity of precipitation is color coded (units—dbZ)

## Slide 11: Reading a Radar Image (color scales can vary)
Black (white in some)-no precip
Grey and pink (5-20 dbZ)…light rain…not too bad.
Dark pink to green-moderate rain (20-35)
Yellows are heavy rain 40-50 (forget it)
Reds and higher (very heavy rain or hail)

## Slide 12: Reading a Radar Image
Radar beam can be blocked by mountains
Time is in UTC (GMT).

## Slide 13: Radar Imagery is generally not observed or displayed for a level surface
Radars scan in azimuth ( 0 to 360 degrees) at a series of increasing scan angles from the horizontal.

## Slide 15: Radar image does not show a single level, but a sloping cut through the atmosphere
Thus showing precipitation higher and higher up in the atmosphere as you move away from the center of the radar image.
https://www.youtube.com/watch?v=Yrq2TVdM8HI

## Slide 16: Radar imagery is generally shown on a polar-type chart with range circles at increasing distance
Higher
Lower
Radar
location

## Slide 17
Range circle every 100 km (60 miles)

## Slide 18: Important points
Shallow drizzle often does not appear on radar imagery, particularly when a distance away.
Can only see deep and high-level precipitation at a distance.
Radar beam can be blocked by local terrain.

## Slide 19: Modern Radars are Doppler Radars
Doppler radars can tell the speed of the target towards or away from the radar.
The wavelength/phase of the radar signal changes, depending the speed of the target towards or away from the radar.

## Slide 20: Same principle used in police radar guns

## Slide 21: Based on Doppler Effect: evident when a train or car passes
https://www.youtube.com/watch?v=a3RfULw7aAY

## Slide 22: Doppler Effect for Weather Radars
The ”targets” are generally precipitation particles (rain drops, snow flakes)…but can include birds, bugs, and even tornado debris.
Meteorological targets generally move with the wind…so we get wind information from Doppler
radar.

## Slide 23: Doppler Radar Imagery: Rarely Shown by the Media

## Slide 24: Lots of uses: such as seeing rotation associated with tornadic thunderstorms

## Slide 25: Weather Radar History

## Slide 26: Radar Was An Important Tool in WWII: Had One Pesky Problem—Precipitation!

## Slide 27: WWII Radars

## Slide 28: After WWII, Meteorologists Experimented with Military Radars: Thunderstorms and Convection Clearly Seen

## Slide 29: Hurricanes Also Apparent in Radar, Including Eye Walls, Rainbands

## Slide 30: In the late 1950’s a national meteorological radar network was established (WSR-57).

## Slide 31: WSR-57 (no Doppler capability)

## Slide 32: During the 1970s and early 80s a lot of experimentation with Doppler Weather Radars
Can show wind shifts and circulations
Diagnose how wind changes with height
Particularly useful for showing the rotation in severe convection—the mesocyclone

## Slide 34
In the late 1980s,
the NWS put in a network of Doppler Weather
Radars:
NEXRAD
WSR88D
(Weather Surveillance Radar 88 Doppler)

## Slide 36
The National Weather Service has Installed Doppler Weather
Radars Across the Country
Available every 5-6 minutes

## Slide 37: Big Radar Advance in 2011: Dual-Polarization

## Slide 38: Can determine precipitation type and more

## Slide 39
Weather Radar Can Change Your Life!

## Slide 40: Weather Radar Can Help You Plan Outdoor Activities
Available every 5-6 minutes
Animations tell you what WILL happen
Since the National Weather Service put the Camano Island weather radar in place during the early 90s, I rarely get seriously soaked while commuting by bicycle.
With a little knowledge of NW precipitation and weather radar, you can protect yourself too.

## Slide 41: Examples
After fronts go through, we often have showers and sun breaks. Radar allows you to stay in the breaks

## Slide 42: Showers as seen in weather radar, simply wait a few minutes for heavy rain to end

## Slide 43
Puget Sound Convergence Zone: Go north or south to stay dry!

## Slide 44
Puget Sound Convergence Zone: Very Narrow Zone of Rain

## Slide 45
Rainshadows: Find them with weather radar
Windward
Enhancement
Rainshadow

## Slide 47: Where to view radar imagery
On TV
On the web
Dedicated app
Radarscope: My Favorite Radar App

## Slide 48: Radar Imagery Available on Atmospheric Sciences Department website

## Slide 49: https://a.atmos.washington.edu/weather/radar.shtml