## Slide 1
Sunlight is Free: How Atmospheric Scientists help Harness it
Manajit Sengupta
University of Washington, Seattle, WA
July 14th, 2018

## Slide 2: The Fuel is Free…but Variable
*1 Barrel of Oil = 1.7MWh
Credit: DOE
In one average day at NREL,
an area of 236 m2 receives 1.7MWh of solar radiation
~13 parking spaces = 1 BOE/day
  Understand the Weather-Driven
  Renewable Energy FUEL Supply:
  Characterize renewable energy density which varies with TIME and LOCATION

## Slide 3
Reduce solar deployment, financing and operational costs.
How is Solar Resource Information Applied
Source: https://www.nrel.gov/docs/fy18osti/68886.pdf

## Slide 4: What are our Research Objectives?
1. Improve accuracy and reduce costs of solar measurements.
4. Disseminate accurate solar resources information
2. Develop accurate solar resource data products and models
3. Develop & publish standards and best practices for solar measurement and modeling
Impact: Easily accessible, high-quality solar resource information reduces the cost of solar prospecting, financing, deployment and operations.

## Slide 5
Measurement and Standards

## Slide 6: How uncertain is our best measurement?
Sources of Measurement Uncertainty
Calibration
Spectral response
  Zenith angle response
  Maintenance-Soiling
  Data logger uncertainty
  Temperature dependence
  Nonlinear response
  Thermal offset
  Instrument aging

## Slide 7: Comparing Radiometers under All-sky Conditions

## Slide 8: Can we evaluate long-term variability?
GHI measurements using PSP from 1981.
Factory calibration used initially.
NREL calibration process changed over the years.
Thermal offset correction needed for this instrument but was only used in later years.

## Slide 9: Standardization Helps
E824-10 Standard Test Method for Transfer of Calibration From Reference to Field Radiometers (Calibration Standard)
G173-03(2012) Standard Tables for Reference Solar Spectral Irradiances: Direct Normal and Hemispherical on 37° Tilted Surface (Modeling standard)
G183-15 Standard Practice for Field Use of Pyranometers, Pyrheliometers and UV Radiometers (Deployment standard)
ISO – 9060 – Specification and classification of instruments for measuring hemispherical solar and direct solar radiation, (Classification Standard)
E927-10(2015) Standard Specification for Solar Simulation for Photovoltaic Testing (Technology Evaluation standard)
Standards reduce the cost of doing business – essentially reducing the cost of generating electricity from renewable technologies.

## Slide 10
Modeling Solar Radiation

## Slide 11: The National Solar Radiation Data Base
248 weather stations with 26 Solar measurement stations [ERDA, NOAA, 1979]
239 modeled stations with 56 partial measurement stations
[DOE, NOAA, 1994]
1,454 modeled locations
[DOE, SUNY-A, NOAA, 2007]
Satellite-based, gridded, 4 km x 4 km, half-hourly [DOE, NOAA, UW, SCS 2016]
http://nsrdb.nrel.gov
SOLMET 1977–80
NSRDB 1961–1990
NSRDB 1991–2005
NSRDB 1991–2010
1,454 modeled locations
[DOE, CPR, 2012]

## Slide 12: The Physical Solar Model (PSM) Framework

## Slide 13: Solar Energy Models are Empirical and Time-Efficient
Solar Energy
Meteorology
Solving the radiative transfer equation for clear and cloudy conditions
Time-consuming.
Regression and parameterization
Mostly for clear sky
Time-efficient.
The Simple Model of the Atmospheric Radiative Transfer of Sunshine (SMARTS) computes clear-sky solar irradiances in 2002 wavelengths using <0.1 second.

## Slide 14: Fast All-sky Radiation Model for Solar applications (FARMS)
Xie et al., Solar Energy (2016)

## Slide 15: Parameterization of Cloud Transmittance and Reflectance
Cloud transmittances are parameterized as exponential functions of cloud optical thickness and solar zenith angles.
Cloud reflectances are parameterized using simple equations of cloud optical thickness.

## Slide 16: FARMS Is as Accurate as RRTMG
RRTMG
FARMS
GOES satellite data are collocated to a U.S. Department of Energy Atmospheric Radiation Measurement (ARM) Southern Great Plains (SGP) site. The satellite-based retrievals of cloud properties are used as inputs to two-stream and FARMS. A total number of 9,669 scenarios associated with cloudy-sky conditions are selected during 2009–2012.

## Slide 17: FARMS Is Much More Time-Efficient
Computation of cloud T for 39 cloud optical thicknesses, 28 particle sizes, and 50 solar zenith angles
Computation of solar radiation for 9,669 scenarios of cloudy-sky conditions over ARM SGP
32 min.
3 h, 30 min.
0.018 s
2 s
13 min.
2 h

## Slide 18: Validating the NSRDB
GHI: NSRDB Version 3
GHI: NSRDB Version 2
Difference between the two versions:
MERRA-2 hourly AOD vs monthly AOD
Precipitable water vapor from MERRA2
Surface Albedo from MODIS and Snow Cover from IMS
Time shifting method on GOES East.

## Slide 19: Making Technology Viable
DNI Version 2
DNI Version 3
GHI Version 2
GHI Version 3

## Slide 20: New Challenges
Developing cheaper instruments with low maintenance but similar accuracy – used of photodiodes and LED’s
Improving cloud property and aerosol retrievals using next-generation satellites (GOES-16)
Forecasting solar radiation at various time-scales – sub-hourly to days ahead
The biggest challenge: Keep Tom’s legacy of excellence going!

## Slide 21
Handing over to the next-generation:
Tom’s retiring!
Pourna’s off to college!
Can assure you that the future is in good hands.